Ripple Carry Adder
Date: 1 September 2023

Half Adder:
input a,
input b,
output sum,
output cout
Code:
assign sum = a ^ b;
assign cout = a & b;
endModule;;

Full Adder:
input a,
input b,
input cin
output sum,
output cout
Code:
wire t1, t2, t3;
halfadder_name h1(a, b, t1, t2);
halfadder_name h2(t2, cin, sum, t3);
assign cout = t2 | t3;

Ripple Carry Adder:
input [7:0] a,
    input [7:0] b,
    input cin,
    output [7:0] sum,
    output cout

Code:
wire c1, c2, c3, c4, c5, c6, c7;
full_add f1(a[0],b[0], cin, sum[0], c1);
full_add f2(a[1],b[1], c1, sum[1], c2);
full_add f3(a[2],b[2], c2, sum[2], c3);
full_add f4(a[3],b[3], c3, sum[3], c4);
full_add f5(a[4],b[4], c4, sum[4], c5);
full_add f6(a[5],b[5], c5, sum[5], c6);
full_add f7(a[6],b[6], c6, sum[6], c7);
full_add f8(a[7],b[7], c7, sum[7], cout);

8 bit Substracter using full_adder
Date: 8 September 2023

Ripple Carry Adder:
input [7:0] a,
    input [7:0] b,
    input bin,
    output [7:0] diff,
    output bout
Code:
wire b1, b2, b3, b4, b5, b6, b7;
full_add f1(a[0],~b[0], bin, diff[0], b1);
full_add f2(a[1],~b[1], b1, diff[1], b2);
full_add f3(a[2],~b[2], b2, diff[2], b3);
full_add f4(a[3],~b[3], b3, diff[3], b4);
full_add f5(a[4],~b[4], b4, diff[4], b5);
full_add f6(a[5],~b[5], b5, diff[5], b6);
full_add f7(a[6],~b[6], b6, diff[6], b7);
full_add f8(a[7],~b[7], b7, diff[7], bout);